## Slide 1: The Mathematical and Scientific Basis for Developing and Setting Epidemiological Cut-offs (ECOFFs)
John Turnidge
January, 2018

## Slide 2: Topics: Questions I will try to answer
What is an MIC, mathematically speaking?
Why the 2-fold dilution series?
How are wild-type MICs distributed?
Why are wild-type MICs distributed that way?
What is the intended objective of ECOFFs?
What method should we use for ECOFF estimation?

## Slide 3: Topics: Answers in brief…
What is an MIC, mathematically speaking?
  an interval measure
Why the 2-fold dilution series?
  a happy accident of history
How are wild-type MICs distributed?
  anything but wildly
Why are wild-type MICs distributed that way?
  because of variations

## Slide 4: Topics: Answers in brief…
What is the intended objective of ECOFFs?
  intention will influence the choice of ECOFF
What method should we use for ECOFF estimation?
  several to choose from…

## Slide 5: What is an MIC, mathematically speaking?
MICs are mostly measured on the two-fold dilution scale
The two-fold dilution scale is an interval scale
It is a scale of ‘convenience’, allowing us to rapidly quantify the phenotype, but any other scale is possible, e.g.
  the scale on the Etest® strip
  or the ‘half-step’ scale: ...0.5, 0.7 , 1 , 1.4 , 2 , 2.8…

## Slide 6: What is an MIC, mathematically speaking?
It is possible to measure MICs on even finer scales, but…
  it isn’t practical for large numbers of tests
  the benefits are not obvious (they are there!)
  it increases the risk of ‘skip’ wells
  there is a limit, which is bug-drug dependent
    e.g. Soothill et al., JAC 1992; 29: 137-139; colonies formed from an individual CFU in an inoculum have a range of MICs
Agar dilution, P. aeruginosa, gentamicin, arithmetic scale
of dilutions, ~20 CFU per drop.
~0.25 – 0.45

## Slide 7: What is an MIC?
Less obviously, the MIC values that we normally assign are actually at the upper end of the interval
  that’s because, for instance, a strain that grows up to a concentration of 1.5 mg/L, but not higher, will grow at 1 mg/L but not at 2 mg/L, and it’s MIC will be recorded as 2 mg/L (not as 1.6 mg/L say) in our two-fold dilution series

## Slide 8: What is an MIC?
The way the data are usually presented…
| | | | | | |
≤ 0.25 0.5 1 2 4 8 ≥16

## Slide 9: What is an MIC?
The correct way to present the data…
| | | | | | |
≤ 0.25 0.5 1 2 4 8 ≥16

## Slide 10: What is an MIC?
Or mathematically, as a formal histogram on a log2 scale…
“(“ means down to but not including
“]” means up to and including
Interval labels

## Slide 11: Why the two-fold dilution scale?
The two-fold scale is a logarithmic scale
Which seems to have started with Alexander Fleming in 1929…

## Slide 12: How are wild-type MICs distributed?
As it turns out, a logarithmic scale is the right thing to use…
  it follows from the law of mass action as it applies to drug-receptor interactions, which is what is being measured indirectly*
MICs are distributed on a Log-Normal scale
  or as near to Log-Normal as can be estimated on the (rather coarse) two-fold dilution interval scale
  note that the Log-Normal scale has no lower or upper bound, i.e. doesn’t come with an ‘in-built’ ECOFF
* Riggs DS, 1963. The Mathematical Approach to Physiological Problems. The MIT Press, Cambridge, MA. pp 286-296

## Slide 13: How are wild-type MICs distributed?
There are many other “bell curve” shaped symmetrical distributions other than the Normal = Gaussian, especially the Logistic (related to the Hill equation that we use for PK-PD exposure-response curves)
The two-dilution scale that we use is surprisingly rather coarse and therefore it is not possible to show which “bell curve” is the best fit
Normal distribution
Cumulative normal distribution
Logistic distribution
*Wadsworth. Handbook of Statistical Methods for Engineers and Scientists, 2nd Ed..1998. p 6.6

## Slide 14: How are wild-type MICs distributed?
In most circumstances, the Normal distribution is preferred, as it is a consequence of the central limit theorem, which deals with distributions that are the sum of multiple sources of variation*
The cumulative Normal distribution is especially valuable for the analysis of MIC distribution data because it automatically models results when the values which are at the upper end of the interval scale
Cumulative normal distribution

## Slide 15: Why are wild-type MICs distributed that way?
Variations!
  Assay variation
    reagents
    intra-laboratory (reading)
    inter-laboratory (conditions)
  Biological variation
    strain-to-strain
We have some information on this now for disk diffusion, but not much for broth microdilution
Biological variation contributed between 10.4% and 98.8% of the variances for different bug-drug combinations

## Slide 16: Why are wild-type MICs distributed that way?
Variations!
  Assay variation
    reagents
    intra-laboratory (reading)
    inter-laboratory (conditions)
  Biological variation
    strain-to-strain
Same strain, same batches of reagents

## Slide 17: What is the intended objective of ECOFFs?
To separate wild type from non-wild type?
  only when there is little or no overlap with non-wild type
To ensure resistance mechanisms are detected?
  requires a knowledge of all resistance mechanisms
To ensure the ‘upper end’ of the wild type is captured?
  overlap would have to accepted
To align with molecular resistance detection?
  ECOFFs are about the phenotypic expression
Gunnar will address this

## Slide 18: How well does the ECOFF separate wild type from the non-wild type?
Variations in wild type versus non-wild type
Log2 Mean Wild-Type MIC = –3.5 Log2 Mean Non-Wild Type MIC = 2.5
Log2 SD Wild-Type MIC = 0.75 Log2 SD Non-Wild Type MIC = 0.75
ECOFF

## Slide 19: How well does the ECOFF separate wild type from the non-wild type?
Log2 Mean Wild-Type MIC = –2.5 Log2 Mean Non-Wild Type MIC = 1.5
Variations in wild type versus non-wild type
ECOFF

## Slide 20: How well does the ECOFF separate wild type from the non-wild type?
Log2 Mean Wild-Type MIC = –1.5 Log2 Mean Non-Wild Type MIC = 0.5
Variations in wild type versus non-wild type
ECOFF?

## Slide 21: How well does the ECOFF separate wild type from the non-wild type?
Log2 Mean Wild-Type MIC = –1.5 Log2 Mean Non-Wild Type MIC = 0.5
Skewed
Variations in wild type versus non-wild type
ECOFF?

## Slide 22: How well does the ECOFF separate wild type from the non-wild type?
Log2 Mean Wild-Type MIC = –0.5 Log2 Mean Non-Wild Type MIC = 0.5
Variations in wild type versus non-wild type
ECOFF?

## Slide 23: How well does the ECOFF separate wild type from the non-wild type?
Log2 Mean Wild-Type MIC = –0.5 Log2 Mean Non-Wild Type MIC = 0.5
Skew is difficult to see
Variations in wild type versus non-wild type
ECOFF?

## Slide 24: What method should we use for ECOFF estimation?
The visual estimation (“eyeball”) method
  Kahlmeter
The 95% rule
  Pfaller et al., J Clin Microbiol 2009
The Normalised Resistance Interpretation
  Kronvall, J Clin Microbiol 2010
The iterative statistical method
  Turnidge, Kronvall, Kahlmeter, Clin Microbiol Infect 2006
Multimodal analysis
  Meletiadis et al., Antimicrob Agents Chemother 2012
Multinomial method
  Jaspers et al., Stats in Med 2014
The second derivative method
  Meletiadis et al, Antimicrob Agents Chemother 2017
If there are many methods, it’s likely that none are perfect!

## Slide 25: Visual estimation method
As currently displayed for almost all distributions on the EUCAST MIC website
Visual estimation of symmetry and proportions
e.g. E. coli - gentamicin https://mic.eucast.org/Eucast2/regShow.jsp?Id=908

## Slide 26: The 95% Rule
Pfaller et al., J Clin Microbiol 2009

## Slide 27: Normalized Resistance Interpretation
Uses an adaptation of a method originally devised for “ECOFFs” for zone diameter distributions
  Kronvall et al., Clin Micro Infect 2003; 9:120-132

## Slide 28: Normalized Resistance Interpretation
Chart: MIC
| 0.125 | 0.18 | 0.25 | 0.35 | 0.5 | 0.7 | 1 | 1.4 | 2 | 2.8 | 4 | 5.7 | 8 | 11.3 | 16 | 22.6 | 32 | 45.3 | 64 | 90.5 | 128
West | 7 | 176 | 345 | 925 | 1505 | 1665 | 1825 | 1000.5 | 175 | 93 | 31 | 0 | 0 | 0 | 0 | 0 | 0 | 624 | 1218 | 1432 | 1646
Original distribution
Kronvall, J Clin Microbiol 2010; 48:4445-4452
Implemented in Automatic NRI calculations for MIC distributions, Excel beta-version http://www.bioscand.se/nri/

## Slide 29: Normalized Resistance Interpretation
Chart: MIC
| 0.125 | 0.18 | 0.25 | 0.35 | 0.5 | 0.7 | 1 | 1.4 | 2 | 2.8 | 4 | 5.7 | 8 | 11.3 | 16 | 22.6 | 32 | 45.3 | 64 | 90.5 | 128
West | 7 | 176 | 345 | 925 | 1505 | 1665 | 1825 | 1000.5 | 175 | 93 | 31 | 0 | 0 | 0 | 0 | 0 | 0 | 624 | 1218 | 1432 | 1646
Implemented in Automatic NRI calculations for MIC distributions, Excel beta-version http://www.bioscand.se/nri/
Dummy values
Line of best fit
Mean and SD calculated from line of best fit
ECOFF = Mean* + 2 x SD then rounded up
(*Mean adjusted down in an unspecified manner)
Kronvall, J Clin Microbiol 2010; 48:4445-4452

## Slide 30: Normalized Resistance Interpretation
Example from original publication
Kronvall, J Clin Microbiol 2010; 48:4445-4452
Implemented in Automatic NRI calculations for MIC distributions, Excel beta-version http://www.bioscand.se/nri/

## Slide 31: Iterative Statistical Method
Turnidge et al., Clin Microbiol Infect 2006; 12(5):418-25.

## Slide 32: Iterative Statistical Method
Converts MICs to log2 values
Repeatedly estimates for each subset above the (left-hand) mode for the cumulative distribution the
  mean MIC
  SD and
  subset total
Selects the mean and SD from the subset whose total is closest to the actual subset total
Creates a list of ECOFFs against desired percentages of the wild-type (multiples if SD above mean), rounded up (implemented in ECOFFinder and MicDat)
Turnidge et al., Clin Microbiol Infect 2006; 12(5):418-25.

## Slide 33: ECOFFinder – raw data entry

## Slide 34: ECOFFinder – preparing the analysis
Cumulative values

## Slide 35: ECOFFinder – running the analysis

## Slide 36: ECOFFinder – reviewing the results

## Slide 37: Iterative Statistical Method - MicDat

## Slide 38: Multimodal Method
Meletiadis et al., Antimicrob Agents Chemother 2012; 56(5):2524-9.

## Slide 39: Multimodal Method
If necessary, enrich the putative non-wild type
Plot the data against Normal quantiles*
Confirm presence of two distributions using non-linear least squares regression
Validate the cut-offs using recursive partitioning*
*requires commercial software unless you’re great at Excel!

## Slide 40: Multinomial method

## Slide 41: Multinomial method
Uses a non-parametric maximum likelihood-based inference on a mixture:
Compared Log-Normal distribution with the Gamma distribution by repeated analysis of expanding subsets
Compared their method to the iterative statistical method
Software not specified
“…we require clear separation between the wild-type and non-wild-type population.”
ECOFFs set at 99.9% of the estimated wild-type population, rounded up
Jaspers et al., Stat in Med 2014; 33:289-303

## Slide 42: Second derivative method
Based on the concept that there is a type of ‘cut-off’ on a bell-shaped curve where there is a maximum change in slope
  the point above the mean of greatest convexity (≈1.73 SD for a Normal distribution)
Uses numerical differentiation to avoid making assumptions about the underlying distribution
Option in GraphPad Prism™ software, but easily done in Excel
Meletiadis et al., Antimicrob Agents Chemother 2017; 61(4):e02372-16

## Slide 43: Second derivative method
Maximum point on graph indicate the dECOFF
Produces a only single ECOFF
Easily applied to data on any scale
Can cope with some left-truncated distributions
Meletiadis et al., Antimicrob Agents Chemother 2017; 61(4):e02372-16

## Slide 44: Method comparison
Method | Accessibility | Multimodal performance | Overlap performance* | Caveats
Visual estimation | Anyone can do it | Good | Good | Subjective; can’t be codified
95% rule | Anyone can do it | Poor | Poor | Only works with unimodal data
NRI | Software downloadable | Good ?better | Good | Requires dummy variables; not mid-point adjusted Patented; research purposes only
Iterative statistical | Software downloadable | Good | Good | User chooses ECOFF percentage
Multimodal | Commercial software needed | Good | Good | Can’t cope with unimodal data
Multinomial | Not accessible | Good | ?? | Sophisticated statistical skills and software needed
Second derivative | GraphPad Prism or develop your own | Good | Poor | Single value output; no options Copes with some truncated data
*Selecting ECOFFs when there is significant overlap depends on the desired interpretation

## Slide 45: Conclusions 1
MICs are measured on a logarithmic scale and follow a “bell-shaped” distribution in the wild type
The Log-Normal distribution model is suitable for almost all purposes
The observed wild-type distribution is mixture of biological, reagent, reading and test condition variation
The selection of ECOFFs ultimately depends on the intended application; or expressed differently, on whether sensitivity or specificity is prioritised!
There are a variety of methods for estimating ECOFFs
  all are vulnerable to overlap between wild type and non-wild type
  they sometimes agree!

## Slide 46: Conclusions 2
There are a variety of methods for estimating ECOFFs
  all are vulnerable to overlap between wild type and non-wild type
  choose one(s) to suit the intended application, considering each of the following criteria:
    accessible
    easy to use
    adjusts to the mid-points of the MIC intervals
    works with both unimodal and multimodal MIC distributions
    works with overlapping distributions, within reason

## Slide 47: Conclusions 3
The (reference) MIC assay, as it is currently performed, can be taken to be a ‘robust’ measure of susceptibility, given that it is :
  performed using non-standardized materials (plastics, broth ingredients)
  on very variable species and strains
  under imperfectly-defined conditions (inoculum, temperature, duration)
  read by imperfect humans
Despite its limitations, we have to learn to understand it properly and make the most of it
  and try to avoid truncation when generating distributions